## Slide 1: Logic Gates & Use of Boolean Algebra
By Amila Giragama,
IT Systems,
Polgahamula.

## Slide 2: Main Target Area
Boolean Algebra
Basic Laws in Boolean Algebra
Logic Gates
Please Turn Off Your Mobil Phones
The Greek philosopher
Aristotle
is the founder

## Slide 3
Find The Answer
=8
=9
=10
=11
=12
=13
=14
=15
=16
=17
=18
=Other
6
7
13
14
12
17
15
11
8

## Slide 4: Algebraic Expression
When numbers, letters, digits, mathematical operators, variables and plus or minus signs are arranged to get a mathematical or logical idea we call it an algebraic expression.
They Should not contain an equal Sign
4a+5b
-7x+y-2z
3l+2m+n
X=Y+3

## Slide 5: Algebraic Equation
Two algebraic expressions connected by an equal sign
Profit=Income-Expenditure
v=u+ft
(x−h)+(y−k)=r
2
2
2

## Slide 6: Boolean Algebra
Boolean Values
  To express Boolean values
    ‘True’ or ‘False’
    ‘1’ or ‘0’
Boolean Expression
  If any expression gives only logical values as a result, it is defined as a Boolean Expression
    The sun is a cold object
    3 > 4
Boolean Variables
  Variable can take only logical variables

## Slide 7: Boolean Operations
OR – Boolean Addition
AND - Boolean Multiplication
NOT - Boolean Complementation

## Slide 8: OR – Boolean Addition ( + )
+ sign is use for the addition operation in Boolean Algebra. This is known as “OR”.
If A and B are Boolean variables, let us consider the expression ‘A+B’ (A OR B)
A | B | A+B (A OR B)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Truth Table
If and only if the values of both variables A and B are 0, A + B is 0.
In all other situations A + B =1

## Slide 9: AND – Boolean Multiplication ( . )
We user “.” sign or ‘AND’ operation
If A and B are two Boolean variables, let us consider the expression ‘A.B’ (A AND B)
A | B | A+B (A OR B)
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Truth Table
If and only if the values of both variables A and B are 1, A . B is 1.
In all other situations A . B = 0

## Slide 10: NOT – Logic Complement ( -/’ )
For ‘NOT’, operation we user “-” (bar) or “ ’ ”
If A is the Boolean variable, let us consider the expression NOT A.
A | NOT A (Ā)
0 | 1
1 | 0
Truth Table
For the operation NOT only one variable is used

## Slide 11: OR Gate

## Slide 12: AND Gate

## Slide 13: NOT Gate

## Slide 14: Review
Boolean addition is equivalent to the OR logic function, as well as parallel switch contacts.
Boolean multiplication is equivalent to the AND logic function, as well as series switch contacts.
Boolean complementation is equivalent to the NOT logic function, as well as normally-closed relay contacts.

## Slide 15: Simplification of Boolean Expression
Start from the left and move towards the right.
First simplify operation within brackets.
After then do all NOT operations (¯) from left to right
Then do AND operation (.) from left to right
Finally do OR operation (+) from left to right

## Slide 16
Construct Truth Table for the fallowing Boolean expression
  A.B+A.Ā
  (A.B).A +(A.B).B
  A+Ā.B
Find the values of fallowing Boolean Expressions
  1.1.0 + 1.1.1+0.1+1
  -----

## Slide 17: Basic laws of Boolean Algebra
Commutative Law
  X+Y=Y+X
  X.Y=Y.X
Let X, Y and Z be Boolean variables.
X=0, if and only if X ≠1
X=1, if and only if X ≠0
X+0=X
X.0=0
X+1=1
X.1=X
Associative Law
  X+(Y+Z)=(X+Y)+Z
  X.(Y.Z)=(X.Y).Z
Idempotent Law
  X+X=X
  X.X=X
Distributive Law
  X.(Y+Z)=X.Y+X.Z
  X+Y.Z=(X+Y).(X+Z)

## Slide 18: Basic Laws Cont……

## Slide 19
Another identity having to do with complementation is that of the double complement:

## Slide 21
De Morgan’s Law
  X+Y=X.Y
  X.Y=X+Y